## Slide 1: SUGAR LOAF COUNTY ROUTE 13 DEDICATION BENEFITS 10/25/21
Existing Conditions
Non-standard road features exist that do not conform to CR spec
  Parking and buildings close to roadway
  Sidewalks too close to road
Sidewalks issues:
  Not ADA compliant
  No IMA exists (County policy for IMA’s to be in place requiring local municipality to maintain sidewalks within County ROW)
  Constructed of inconsistent materials
  Not enough separation between sidewalks and roadway/parking
  In and out of private properties
  County at a standstill issuing sidewalk permits
High pedestrian traffic
Unwanted heavy truck traffic
Speeding vehicles
Overall businesses are said to be struggling due to pedestrian access and safety concerns
Town has requested ownership of the road
Inappropriate temporary weight (10 Ton) limit signing should be removed. County policy is to restrict bridges only with few exceptions.
County roads are intended to provide intercounty travel corridors, we strive to reduce restrictions to travel, such as weight restrictions, etc. along County Roads. The Town and businesses are looking to do the opposite here. Hence the SugarLoaf bypass was built.

## Slide 2: SUGAR LOAF COUNTY ROUTE 13 DEDICATION
Benefits
The Sugar Loaf by-pass was specifically created to take through traffic around the hamlet. This would be more effective if Town was in control of CR-13 and was able to implement traffic calming measures that would encourage through traffic to use by-pass.
Town control of Kings Highway would allow for:
  Signage with a more restrictive and permanent weight restriction
  Potentially placing stop signs at Pine Hill Rd and Creamery Pond Rd(by lyceum theatre)
  Additional cross walks could be added in the center of sugar loaf
  Non-standard traffic calming features
No IMA’s would be needed for sidewalk/curb maintenance
Permits for work along roadway and events/festival permits would be under the control of the Town.
  Special events-Spring and Fall festivals
A quiet roadway should remove the need for an expensive sidewalk project in the hamlet.
Unfettered potential for infrastructure improvements and creation of a Buisness Improvement District
The Town of Chester Board voted in unanimous support of the road transfer
Those most vested in the community will be in control

## Slide 3: SUGAR LOAF COUNTY ROUTE 13 DEDICATION
Other Town Considerations
There are 91 miles of Chester town roads. Adding one additional mile to highway maintenance represents just less than a 1% increase in maintenance costs, which will partially be offset by additional CHIPS money that will be received.
It is anticipated that the lower traffic volume will theoretically result in lower maintenance costs for this section of road.
Business District to be created???
  More flexibility when town owned??